## Slide 1: Classical Mechanics Lecture 15
Today’s Concepts:
  Stress and Strain
Presentation Created by Dr. Adam Lark

## Slide 2: Things you asked about:
Insert student comments from the “lecture thoughts” checkpoint question here!
Add slides that answer specific student comments as needed.

## Slide 3: Young’s Modulus
Rigidity of Material
Represents how difficult to change length of object when applying a force.

## Slide 4: What is Young’s Modulus?
Large Y: Rigid Material
Difficult to change length
Example: Steel Rod
Small Y: Pliable Material
Easy to change length
Example: Rubber Band

## Slide 5: Checkpoint 1
One rod is made of stainless steel (Y = 180 x 109 Pa), the other is made of Titanium alloy (Y = 110 x 109 Pa). Which rod undergoes the greatest change in length?
  Stainless steel rod
    Student Explanation
  Titanium alloy rod
    Student Explanation
  Same for both
    Student Explanation
smaller Y
Greater ΔL

## Slide 6: Checkpoint 2a
A tension is applied to an aluminum rod (Y = 70 Pa) of length 1 m, it stretches by ΔL. If the same tension is applied to another aluminum rod with the same cross-sectional area, but of length 2 m, by how much will it stretch?
  Less than ΔL
    Student Explanation
  ΔL
    Student Explanation
  More than ΔL
    Student Explanation

## Slide 7: Checkpoint 2a
Same!
If Lo’ increases
ΔL’ must increase
  Answer C: More than ΔL

## Slide 8: Checkpoint 2b
Now tension is applied to two aluminum rods of length 1 m, one twice as thick as the other. If a compressive force F is applied to both wires, their lengths are reduced by ΔLthick rod and ΔLthin rod respectively. The ratio ΔLthick rod /ΔLthin rod is:
  ΔLthick rod /ΔLthin rod = 1
    Student Explanation
  ΔLthick rod /ΔLthin rod < 1
    Student Explanation
  ΔLthick rod /ΔLthin rod > 1
    Student Explanation

## Slide 9: Checkpoint 2b
Thin/Thick  area changes!
Same!
(Young modulus equation solved for ΔL)
Answer: B

## Slide 10: Volume Stress/Strain
Bulk Modulus (B):
How much pressure is needed to change the volume of an object
Notice the negative!
As pressure increases
volume decreases
Small Bulk Modulus: pliable
Large Bulk Modulus: rigid
p

## Slide 11: Shear Stress
Shear Modulus (S):
How much Force is needed to deform an object
Small Shear Modulus: pliable
Large Shear Modulus: rigid

## Slide 12: Checkpoint 3a
Three cylinders of the same dimensions (5-cm length and 1.0-cm radius) are each built of a different material: aluminum, brass and glass.

## Slide 13: Checkpoint 3a
Which cylinder will exhibit the largest change in volume when an external pressure is applied to it?
A. Aluminum
B. Brass
C. Glass
Need Bulk Modulus!
Small B, more pliable  Easier to change volume

## Slide 14: Checkpoint 3b
A force of the same strength is applied to the top of each cylinder as shown. Which cylinder will prove more difficult to deform through shear stress?
A. Aluminum
B. Brass
C. Glass
Need Shear Modulus!
Larger S, more rigid  harder to deform

## Slide 15: Breaking Point
At some point, objects can no longer be stretched…
After enough force, the object will permanently deform!